## Slide 1
Specifications and Settings of Logging features
Panasonic Corporation
May 15, 2018
Ver.1.4
(KX-TGP600, KX-HDVx30 series)

## Slide 2
KX-TGP600 and KX-HDVx30 support some logging features in order to troubleshoot issue more earlier and easier.
The engineer check this log from remote site.
This document describes about KX-TGP600 and KX-HDVx30 support logging features.
Abstract about this document
Revision history
Date | Version | Revision | Firmware version
Nov 28, 2016 | Ver. 1.0 | Initial Release | All versions
July 26, 2017 | Ver. 1.1 | Add Function list with capacity to store the log information (page-5) | 
March 9, 2018 | Ver. 1.2 | Add reason of power log information (page-7) | 
Apr 3, 2018 | Ver. 1.3 | Add comment of power log information (page-7) | 
May 15.2018 | Ver. 1.4 | Add Dect monitoring(page-3,5), modify (page-4,5,10) | 

## Slide 3
1. Outline
1.Outline
1. What kind of log can the phone export ?
1. Power Down log
When the phone restarts, the reason of restart is logged.
2. Event log
The internal events of the phone are logged.
It is used to analyze the internal processing of the phone.
3. SIP Packet log
The transmitted and received of SIP packet are logged.
It is used to analyze SIP protocol.
4. Application log (= internal processing log)
5. Operational value (= Actual configuration settings)
6. DECT monitoring log (TGP600 only)
Items | Export via WEB GUI | Export via syslog
Power Down log | ü | -
Event log | ü | ü
SIP Packet log | ü | ü
Application log | - | ü
Operational Value | ü | ü
DECT monitoring | View current status | ü
2. How to export ?
You can export logs via a) WEB GUI or b) Syslog *need to prepare syslog server
Firmware version:
KX-TGP600 V2.104
KX-HDV130 V2.100
KX-HDV230 V2.100
KX-HDV330 V2.100
KX-HDV430 V2.105

## Slide 4
Items | Common setting | Related settings | Note
Power Down log | (none) | (none) | Supported since first version
Event log | a) If you export via WEB GUI, do not specify the syslog server address. ↓ SYSLOG_ADDR =““ (NULL) b) If you export via Syslog, please specify the syslog server address. ↓ SYSLOG_ADDR =“xxx.xxx.xxx.xxx“ | (example) LOGGING_LEVEL_DNS=“6" LOGGING_LEVEL_NW1=“6" LOGGING_LEVEL_FILE=“6" LOGGING_LEVEL_TR069=“6" LOGGING_LEVEL_STUN=“6" LOGGING_LEVEL_NW2=“6" LOGGING_LEVEL_CFGPARSE=“6“ | Supported since first version If you try to get the logs, please set “6” to logging level. Syslog level [0 <-> 6] 6:info -> recommend 5:notice 4:warning 3:error 2:critical 1:alert 0:emergency
SIP Packet log |  | (example) LOGGING_LEVEL_SIP="6" SYSLOG_SIP_PACKET_ENABLE="Y“ | 
Application log |  | SYSLOG_OUT_START “N”->“Y”: Logging Started “Y”->“N”: Logging Stopped | “Logging Started” means the phone starts logging its internal processing log (Application log) and send it to Syslog server in each case. “Logging Stopped” means the phone stops logging Application log. And the phone sends Application log details to Syslog server. Application log (details) -Memory -Process -Ps tree -Power down log -Kernel log -Event log -Handset information (DECT monitoring)
Operational Value |  | (none) | The phone sends Operational Value to Syslog server in each specified user operation.
1. Outline
1.Outline
3. Function list with setting information

## Slide 5
Items | Capacity to store the log | How to delete | Note
Power Down log | 30 logs (events) | can be erased by Factory Reset. | New logs overwrite and older logs will be discarded.
Event log | 500kB (Flash ROM) - Event Log and SIP Trace Log may hold approximately 1 day of events |  | 
SIP Packet log | 500kB (SRAM) - Event Log and SIP Trace Log may hold approximately 1 day of events | can be erased by power off. | 
Application log | 500kB(SRAM) -Internal process log | can be erased by power off. | New logs overwrite and older logs will be discarded
DECT monitoring | Latest 8 handset status in RAM | can be erased by power off. | TGP600 ver07.302 or later Depend on DECT_MONITORING_CYCLIC_INTV and DECT_MONITORING_OUTPUT
1. Outline
1.Outline
4. Function list with capacity to store the log information

## Slide 6
2. Power Down log
No extra configuration parameter setting is necessary.
1)Open Web GUI with CS ID
2)Select “Maintenance” Tab
3)Select “Power Down” (Default setting)
4)Push “Export” button
File “power.log” is saved.
1. Method of exporting via WEB GUI

## Slide 7
Logging class | Format
Power on | 1:PowerOn<tab>FF-FF-FFFF FF:FF:FF<tab>Version=xx.xxx <LF> *note) This log will be outputted AFTER the device boot up, which includes the firmware version running AFTER a boot up process. ( without Soft reset)
Soft Reset | 2:Soft Reset<tab>01-22-2014 13:42:30<tab>Version=xx.xxx <tab>Reason:XXX<LF> *note) This log will be outputted BEFORE a soft reset starts, which includes the firmware version running BEFORE a soft reset process.(there is possibility the running firmware version changes AFTER a soft reset process )
Format of Power down log
data | Explanation | 
FF-FF-FFFF FF:FF:FF 01-22-2014 13:42:30 | Day and time, if endpoint has information. | 
Version=xx.xxx | Firmware version.( Current running Firmware version) | 
Reason:XXX | When Logging class is Soft Reset, it has 3 digits reason code. | 
 | 001 005 006 007 012 013 015 016 018 021 022 023 024 025(Auto Reboot) 025 026 030 031 099 101 | Factory Reset Upgrading FW Restart by User operation TR104 Voice Profile Reset Changing PHY settings Changing VLAN settings Changing VoIP config Changing other settings (P2P etc.) Changing TEL config FLASH error Cwmp Fatal Error RebootIND waiting timeout Carrier Default SIP registration is out in all lines MAC base Client Certificate(30year) is downloaded Client Certificate is changed from MAC base to Model base Write error to Sub CPU Chip Communication failure with Sub CPU Chip Others User Interface fatal error (HDV series )
Example
1:PowerOn<tab>FF-FF-FFFF FF:FF:FF<tab>Version=xx.xxx <LF>
2:Soft Reset<tab>01-22-2014 13:42:30<tab>Version=xx.xxx <tab>Reason:XXX<LF>
2. Power Down log

## Slide 8
1. Configuration parameter setting for each event is necessary.
Set “6” to “LOGGING_LEVEL_DNS” (DNS log)
Set “6” to “LOGGING_LEVEL_FILE” (FILE downloading log)
Set “6” to “LOGGING_LEVEL_CFGPARSE” (Configuration parse log)
Before starting to get log, set “6” to necessary configuration parameter.
( sample of configuration file: config_logging_Event_via_WEB-GUI.cfg )
After getting log
1)Open WebGUI with CS ID
2)Select “Maintenance” Tab
3)Select “Event”
4)Push “Export” button
File “event_log.txt” is saved.
2. Import the following configuration file to turn the setting back to default.
(config_logging_Default.cfg )
3. Event log
1. Method of exporting via WEB GUI

## Slide 9
1. Configuration parameter setting for each event is necessary.
Set “IP address” to “SYSLOG_ADDR”
Set “514” to “SYSLOG_PORT”
Set “6” to “LOGGING_LEVEL_DNS” (DNS log)
Set “6” to “LOGGING_LEVEL_FILE” (FILE downloading log)
Set “6” to “LOGGING_LEVEL_CFGPARSE” (Configuration parse log)
Before starting to get log, set “6” to necessary configuration parameter.
( sample of configuration file: config_logging_Event_via_Syslog.cfg )
2. Start wireshark and reproductive test
3. After getting log
Import the following configuration file to turn the setting back to default.
(config_logging_Default.cfg )
[Note]
Syslog packet format (Syslog packet format is compliant to RFC3164.)
PRI (Facility + Severity) + Header + MSG
3. Event log
2. Method of exporting via Syslog

## Slide 10
Logging class | Message Format
File download failure Setting: LOGGING_LEVEL_FILE=“6” | [SERVICE]File download failure by [(XXX) ¦ no response ¦ check sum error ¦ file error ¦ ･･･] “Download URL” Example: [CFG]File download failure by (404) http://pana.com/123.cfg
DNS query failure Setting: LOGGING_LEVEL_DNS=“6” | [DNS]Query failure by [(XXX) ¦ no response ] “Domain name” Example: [DNS]Query failure by (404) sip.com
Configuration parameter parse failure Setting: LOGGING_LEVEL_CFGPARSE=“6” | [cfgPARSE][param ¦ value ¦ format ¦ multi] error “Input parameter value” “Download URL” Example: (Invalid SIP parameter) [cfgPARSE]param error SIPP_TIMER_T1_1=”1” http://pana.com/123.cfg (Invalid value) [cfgPARSE]value error SIP_TIMER_T1_1=”0” http://pana.com/123.cfg (Missing “”) [cfgPARSE]format error SIP_TIMER_T1_1=0 http://pana.com/123.cfg (Duplicate error) [cfgPARSE]multi error SIP_TIMER_T1_1=”1” http://pana.com/123.cfg
SIP REGISTER failure Setting: LOGGING_LEVEL_SIP=“6” | [SIP(L#)]Registration failure by [(XXX) ¦ no response ] *(L#): Target line number of this event Example: [SIP(L1)]Registration failure by no response
Format of Event log
3. Explanation of log
3. Event log

## Slide 11
3. Event log
Jan 1 00:01:06 KX-TGP600JP local2.info INITIAL: mac:080023CE6218 <6> [INITIAL]File download failure by "The requested URL returned error: 404 Not found(404)[E22]" https://provisioning.e-xxxxxxxxx.net:443/xxxxxxx/xxxxxxxx/080023CE6218.cfg
Example
data | Explanation
Jan 1 00:01:06 | Day and time, if endpoint has information.
KX-TGP600JP | Model name
local2.info | [Facility].[Severity] ---(*) refer to RFC3164
INITIAL | Process name
mac:080023CE6218 | MAC address
<6> | Value of [Severity] ---(*) refer to RFC3164
[INITIAL]File download failure by ・・・ | Message
4. Explanation of log with WEB GUI
<150>Jan 1 02:49:06 download: mac:080023CE6218 <6> [FW]File download failure by "invalid file" [-66] http://192.168.1.36/TGP600TPA6x-CE-02.213.fw
data | Explanation
<150> | [Facility] 1001 0 --------- (BIT7-3) Local use2 (19) ---(*) refer to RFC3164 [Severity] 110 ----(BIT2-0) Information (6)
Jan 1 02:49:06 | Day and time, if endpoint has information.
download | Process name
mac:080023CE6218 | MAC address
<6> | Value of [Severity] ---(*) refer to RFC3164
[FW]File download failure by ・・・ | Message
5. Explanation of log with Syslog

## Slide 12
Configuration parameter settings for SIP packet is necessary.
Set “6” to “LOGGING_LEVEL_SIP”
Set “Y” to “SYSLOG_SIP_PACKET_ENABLE”
( sample of configuration file: config_logging_SIP Packet_via_WEB-GUI.cfg)
Reboot the phone once.
After getting log
1)Open Web GUI with CS ID
2)Select “Maintenance” Tab
3)Select “SIP Packet”
4)Push “Export” button
File “sip_trace_log.txt” is saved.
Import the following configuration file to turn the setting back to default.
(i.e. config_logging_Default.cfg )
4. SIP Packet log
1. Method of exporting via WEB GUI

## Slide 13
Configuration parameter settings for SIP packet is necessary.
Set “IP address” to “SYSLOG_ADDR”
Set “514” to “SYSLOG_PORT”
Set “6” to “LOGGING_LEVEL_SIP”
Set “Y” to “SYSLOG_SIP_PACKET_ENABLE”
( sample of configuration file: config_logging_SIP Packet_via_WEB-GUI.cfg)
2. Start wireshark and reproductive test
3. After getting log
Import the following configuration file to turn the setting back to default.
(config_logging_Default.cfg )
[Note]
Syslog packet format (Syslog packet format is compliant to RFC3164.)
PRI (Facility + Severity) + Header + MSG
4. SIP Packet log
2. Method of exporting via Syslog

## Slide 14
Logging class | Format
SIP packet (sent and received) Setting: LOGGING_LEVEL_SIP=“6” | [SIP(L#)][SEND ¦ RECV]: Src=IP ADDRESS:PORT Dst=IP ADDRESS:PORT SIP message *(L#): Target line number of this event Example: [SIP(L1)]RECV: Src=192.168.0.100:5060 Dst=192.168.0.200:5060 SIP/2.0 200 OK Via: SIP/2.0/UDP 192.168.0.200:5060;branch=a1b2c3d4e5f6g7h From: <sip:123456789@sip.win.com>;tag=1234567890 SIP message To: <sip:123456789@sip.win.com>;tag=234567890 Call-ID: 2ab3cde4-2fgh3ijk4lmn5opq6rst7uv8wx9yz000@192.168.0.200 CSeq: 2 REGISTER Contact: <sip:123456789@192.168.0.200:5060>;expires=60Content Length: 0
1. Format of SIP Packet log
4. SIP Packet log
3. Explanation of log

## Slide 15
Jan 1 00:39:19 KX-TGP600JP SIP(L0) RECV[565]: mac:080023CE6218 <6> SIP/2.0 200 OK
Max-Breadth: 60
Via: SIP/2.0/UDP 192.168.1.34:5060;branch=z9hG4bK2c363295
Max-Forwards: 70
Call-ID: 04a53709-eea56f187db91a020e8f0080f0808080@KX-TGP600JP
From: <sip:4502921620@sbc-sundance.metaswitch.com>;tag=668607965
To: <sip:4502921620@sbc-sundance.metaswitch.com>
CSeq: 15 REGISTER
Authorization: Digest realm="sbc-sundance.metaswitch.com",nonce="26895fc6e38a",algorithm=MD5,qop=auth,cnonce="6BAED6F6",nc=0000000e,uri="sip:sbc-sundance.metaswitch.com:5060",username="4502921620",response="93bdf956fee1831c682e0930e795c2d4"
Allow: INVITE,ACK,CANCEL,BYE,PRACK,INFO,UPDATE,OPTIONS,MESSAGE,NOTIFY,REFER
Supported: path
Contact: <sip:4502921620@192.168.1.34:5060>;expires=30
User-Agent: Panasonic-KX-TGP600JP/03.000 (080023ce6218)
Content-Length: 0
Example
4. Explanation of log with WEG GUI
4. SIP Packet log
data | Explanation
Jan 1 00:39:19 | Day and time, if endpoint has information.
SIP(L0) SEND[565] | Process name If the process name is SIP, following additional information is added. (L0): SIP line number. TGP600 has 8 lines, line number 0-7. SEND / RECV: Packet direction. [565]: “565” means process number of Linux.
mac:080023CE6218 | MAC address
<6> | Value of [Severity] ---(*) refer to RFC3164
SIP/2.0 200 OK ・・・ | Message

## Slide 16
<158>Jan 1 01:26:45 SIP(L0) SEND[557]: mac:08002353EB07 <6> REGISTER sip:as.iop1.broadworks.net:5060 SIP/2.0
Max-Breadth: 60
Via: SIP/2.0/UDP 192.168.1.40:5060;branch=z9hG4bK29c41906
Max-Forwards: 70
Call-ID: 5662b013-d4b16f183ffae25efa8b0080f0808080@KX-TGP600(M)
From: <sip:240498020x@as.iop1.broadworks.net>;tag=670105055
To: <sip:240498020x@as.iop1.broadworks.net>
Route: <sip:sbc1.iop2.broadworks.net:5060;lr>
CSeq: 1 REGISTER
Allow: INVITE,ACK,CANCEL,BYE,PRACK,INFO,UPDATE,OPTIONS,MESSAGE,NOTIFY,REFER
Supported: path
Contact: <sip:240498020x@192.168.1.xx:5060>;expires=3600
User-Agent: Panasonic-KX-TGP600(M)/01.xxx (08002353eb07)
Content-Length: 0
Example
5. Explanation of log with Syslog
4. SIP Packet log
data | Explanation
<158> | [Facility] 1001 1 --------- (BIT7-3) Local use3 (19) ---(*) refer to RFC3164 [Severity] 110 ----(BIT2-0) Information (6)
Jan 1 01:26:45 | Day and time, if endpoint has information.
SIP(L0) SEND[557] | Process name If the process name is SIP, following additional information is added. (L0): SIP line number. TGP600 has 8 lines, line number 0-7. SEND / RECV: Packet direction. [557]: “557” means process number of Linux.
mac:08002353EB07 | MAC address
<6> | Value of [Severity] ---(*) refer to RFC3164
REGISTER sip:as.iop1.broadworks.net:5060 SIP/2.0 … | Message

## Slide 17
1. Display the screen of “Embedded Web” by user operation.
1-1. Operation from the phone UI
1. Method of export Application log
2. Enter a digit “**”
-> 1.“Logging Started” is displayed on LCD.
2.Start logging its internal processing log (Application log)
3.Send it to Syslog server in each case.
“**”
Send Application log
in each case
Start logging
Application log
Syslog server
Panasonic
Endpoint
(Idle display)
Export Application log
5. Application log

## Slide 18
4. Enter a digit “##”
-> 1.Stop logging Application log.
2.Send Application log (details) to Syslog server.
3.“Logging Stopped” is displayed on LCD.
4.Logging Application log will finish.
Syslog server
Panasonic
Endpoint
“##”
Send Application log
in each case
Stop logging
Application log
(After “Logging Started”)
Send Application log
(Details)
3. Display the screen of “Embedded Web” by user operation.
(Idle display)
Export Application log
5. Application log

## Slide 19
1-2. Provisioning configuration parameter
Parameter Name | Type | Value Range | Default Value | Explanation
SYSLOG_OUT_START | BOOLEAN | Y/N Y: Enable export application log N: Disable export application log | N | Specifies whether export the application log.
Send Application log
in each case
Start logging
Application log
Syslog server
Panasonic
Endpoint
Provisioning server
Stop logging
Application log
Send Application log
(Details)
1. Provisioning following configuration parameter, SYSLOG_OUT_START=“Y”
-> 1.Start logging its internal processing log
(Application log)
2.Send it to Syslog server in each case.
2. Provisioning following configuration parameter, SYSLOG_OUT_START=“N”
-> 1.Stop logging Application log.
2.Send Application log (details) to Syslog server.
3.Logging Application log will finish.
Download config file
Download config file
Export Application log
5. Application log

## Slide 20
Application log (Sample)
Application log (details) (Sample)
<15>Aug 4 02:04:24 AUDIO[552]: mac:08002353EB07 <7> n=0 Change bandtype from [0] to [2]
<15>Aug 4 02:04:24 TELSH[474]: mac:08002353EB07 <7> HS_NOTIFY_DEVICE_CTP_HS:04000000056401009150000
<15>Aug 4 02:04:24 TELSH[474]: mac:08002353EB07 <7> EVENT_CTP_APP_SETUP:915000002F746D702F637470687
<14>Aug 4 02:04:24 AUDIO[552]: mac:08002353EB07 <6> proc_df_notify_change_bandtype() <===== END =
<14>Aug 4 02:04:24 AUDIO[552]: mac:08002353EB07 <6> proc_df_notify_handset_watch() <===== END ===
<14>Aug 4 02:04:24 AUDIO[552]: mac:08002353EB07 <6> :::::::::::::::::::::::::::::: wait event :::::
<15>Aug 4 02:04:24 CTP[570]: mac:08002353EB07 <7> CtpSendMessage4HsApp::SendMessageToHsApp(): Event
<15>Aug 4 02:04:24 CTP[570]: mac:08002353EB07 <7> EVENT_CTP_APP_SETUP:0000000000000000000000007F000
<15>Aug 4 02:04:24 CTP[570]: mac:08002353EB07 <7> CtpCCState::Execute(): Ins=0, PsId=0, Next State
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> [set_need_dial_plan_check_info] need_dial_p
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> EVENT_CTP_APP_SETUP:00007F0002FFFF0100FFFFF
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> [initialize] hsno.(0)
<14>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <6> do_parallel_mode_action
<14>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <6> check_parallel_info
<14>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <6> get_parallel_group
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> not paired HS
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> [check_parallel_info]parallel_settings is n
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> [check_parallel_info] return PARALLEL_ACT_N
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> [get_configdata] HsNo = 0
<15>Aug 4 02:04:24 DIALTONE[4313]: mac:08002353EB07 <7> [get_configdata] WIDEBAND_AUDIO_ENABLE = 0
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> ################ LOG OUTPUT START!! ######
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> ## SYSTEM DATE AND TIME ##
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> Thu Aug 4 02:05:06 2016
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> ## MEMORY ##
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> MemTotal: 121536 kB
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> MemFree: 36644 kB
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> Buffers: 0 kB
<15>Aug 4 02:05:08 LINKFUNC[4600]: mac:08002353EB07 <7> Cached: 13108 kB
<15>Aug 4 02:05:09 LINKFUNC[4600]: mac:08002353EB07 <7> ## POWER LOG ##
<15>Aug 4 02:05:09 LINKFUNC[4600]: mac:08002353EB07 <7> 2:Soft Reset.FF-FF-FFFF FF:FF:FF.Version=82.009.Reason:001
<15>Aug 4 02:05:09 LINKFUNC[4600]: mac:08002353EB07 <7> 2:Soft Reset.FF-FF-FFFF FF:FF:FF.Version=82.009.Reason:018
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> ## HS INFO ##
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> PSTYPE = TPA60
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> PSTYPE = TPA65
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> get_info : not registerd
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> Usage: test_pstype
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> -s [HSno(1-8)] [PSTYPE] - set PS-TYPE
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> 0:TPA65
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> 1:TPA60
<15>Aug 4 02:05:13 LINKFUNC[4600]: mac:08002353EB07 <7> 2:SIP-DECT
Application log is
Internal processing log for trouble shoot.
If a carrier has trouble and if they provide this log to us, our engineer can investigate details.
(Example) This log indicates follows.
Handset #1 pushed its TALK key and it is hearing Dial tone.
This statement means
this is a beginning point of detail log
Memory status
Power down logs.
Boot up or reboot is logged here.
Handset registering information.
In this case,
Handset #1: TPA60
Handset #2: TPA65
Handset #3: not registered
….

## Slide 21
1. Display the screen of “Embedded Web” by user operation.
1-1. Operation from the phone UI
1. Method of export Operational value
2. Enter a digit “*#”
-> 1.Send Operational value to Syslog server.
The Operational value is divided in each statement.
“*#”
Send Operational value
in each statement.
Syslog server
Panasonic
Endpoint
(Idle display)
Export Application log
6. Operational value

## Slide 22
Operational value (Sample)
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> # Panasonic SIP Phone Standard Format File #
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7>
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> MULTI_NUMBER_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> WIDEBAND_AUDIO_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> CODEC_G722AMR_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> FACTORY_RESET_ENABLE="Y"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> FWD_DND_MENU_ENABLE="Y"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> BLOCK_ANONY_MENU_ENABLE="Y"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> CALL_SETTINGS_MENU_ENABLE="Y"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> ANONY_CALL_MENU_ENABLE="Y"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> SIP_TRUNK_MODE_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> SIP_NON_REGISTER_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> RTP_KEEP_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> AUTO_INPUT_KEY_TIME="0"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> TIME_ZONE_SET_ENABLE="N"
<15>Aug 4 02:02:24 LINKFUNC[4275]: mac:08002353EB07 <7> DISCLOSE_FUNCTION_ENABLE="Y“
…….
Syslog server has Operational value in text file as follows.
1.This statement means
this is a beginning point of Operational value
Procedure how to create Config file from above Operational value text file
1. Find beginning point of Operational value, “# Panasonic SIP Phone Standard Format File #”.
2. Filter in “LINKFUNC” from beginning point forward.
3. Remove description except configuration parameter.
4. Add SIP password information, “SIP_PASS_n”.
2. “LINKFUNC” from beginning point forward means Operational value.
3. Remove this part
# Panasonic SIP Phone Standard Format File #
MULTI_NUMBER_ENABLE="N"
WIDEBAND_AUDIO_ENABLE="N"
CODEC_G722AMR_ENABLE="N"
FACTORY_RESET_ENABLE="Y"
FWD_DND_MENU_ENABLE="Y"
BLOCK_ANONY_MENU_ENABLE="Y"
CALL_SETTINGS_MENU_ENABLE="Y"
ANONY_CALL_MENU_ENABLE="Y"
SIP_TRUNK_MODE_ENABLE="N"
SIP_NON_REGISTER_ENABLE="N"
RTP_KEEP_ENABLE="N"
AUTO_INPUT_KEY_TIME="0"
TIME_ZONE_SET_ENABLE="N"
DISCLOSE_FUNCTION_ENABLE="Y"
…….
Config file
Operational value
in text file